## Slide 1: ISA Documentation Overview
By: Noah Huppert & Robert Scibelli

## Slide 2: General Requirements
General Purpose
32 bit word size
Using Little Endianness
2^32 bit address space
Princeton memory organization

## Slide 3: Supported Data Types
32 bit two's complement integer
32 bit unsigned integer
32 bit IEEE 754 float

## Slide 4: Registers
32 32 bit registers
R0-R27 - general purpose registers
R28: Program counter
R29: Status code
R30: Stack pointer
R31: Return address

## Slide 5: Status Codes
Binary | Assembly | Meaning
0000 | NE | Not Equal
0001 | E | Equal
0010 | GT | Greater than
0011 | LT | Less than
0100 | GTE | Greater than or equal to
0101 | LTE | Less than or equal to
0111 | OF | Overflow
1000 | Z | Zero
1001 | NZ | Not Zero

## Slide 6: Status Codes Specifically for Float
Binary | Assembly | Meaning
1010 | UF | Underflow
1011 | NAN | Not a number
1100 | NM | Normalized
1101 | INF | Infinity
1110 | MS | Mantissa sign
1111 | ES | Exponent sign

## Slide 7: About the Instructions
Group By type: ALU, Mem, and Control
We will be using specific addressing modes as needed
Assembly structure
  {Operation}{Type} <DEST> <OP1> <OP2>
Bit ordering
Condition | Type | Opcode | DEST | OP1 | OP2 | Extra
4 bits | 2 bits | 5 bits | 4 bits | 4 bits | 4 bits | 9 bits
Condition | Type | Opcode | DEST | OP1 | Immediate | Extra
4 bits | 2 bits | 5 bits | 4 bits | 4 bits | 8 bits | 5 bits

## Slide 8: Arithmetic Logic Unit instructions
Add
Subtract
Multiply
Divide
Compare
Shift
  Arithmetically and Logically
And
Or
Xor
Not

## Slide 9: Memory Instructions Control Instructions
Load
Store
Push
Pop
Move
Jump
  Conditionally and unconditionally

## Slide 10: Questions?